## Slide 1: Detectors for MuSR
Erik Schooneveld, Steve Cottrell, Daniel Pooley, Lakshan Ram, Nigel Rhodes
STFC, ISIS facility, UK
Industry day, SINE2020
13th June 2017

## Slide 2: Introduction
MuSR: Muon spin spectroscopy
Study of magnetic fields inside materials
4 facilities: Triumf, Canada
ISIS, United Kingdom
PSI, Switzerland
J-PARC, Japan

## Slide 3: Introduction
Principle
Basically “simple” detector
e+

## Slide 4: Detectors
HAL-9500 (PSI), 32 detectors
Detector module

## Slide 5: Detectors
EMU (ISIS), 96 detectors

## Slide 6: Detectors
Specifications:
Position sensitivity: 1 cm2 (used to be 10-100 cm2)
Number of detectors: ~100
Work in high magnetic fields (2000 times kitchen magnet)
Count rate capability (ISIS): > 10 MHz (10 ns pulse width)
Timing accuracy:  < 100ps (PSI), 1ns (ISIS)
Notes: 200.000 earth magnetic field

## Slide 7: Detectors
Modern detectors:
Could fulfil al requirements.
Plastic scintillator
Light guide
Light sensor + electronics
Detector element of ALC (PSI)

## Slide 8: Detectors
Photomultiplier tube (PMT). SiPM / MPPC
Light sensor

## Slide 9: Detectors
Light sensor properties
SiPM is most promising
Properties | PMT | SiPM
Light sensitivity | 25% | 50%
Gain | 107 | 106
Signal duration | 2ns | 50ns
Timing accuracy | 150ps | <100ps
Noise counts (kHz/mm2) | 0.01-0.1 | >100
Magnetic sensitivity | high | none
Temperature sensitivity | Low | Medium
Area | ~10-1000mm2 | 10mm2
Life time | Very long | Medium

## Slide 10: Requirements
Produce as much light as possible
Produce short flash of light
Commercially available
Not vary with temperature variations
Long life time
Plastic scintillator

## Slide 11: Requirements
Efficient light transport
Shortest light pulses
Commercially available
Robust
Fibre

## Slide 12: Requirements
Light sensor (SiPM)
High sensitivity + gain (large signals)
Very good timing accuracy
Short signal duration
Commercially available
Low temperature sensitivity
Low noise
Long life time

## Slide 13: Requirements
Electronics:
Very fast + process small analogue signals
Compact + size tailored to detector
Acceptable power dissipation
Usually designed in-house

## Slide 14: Challenges
Higher magnetic fields  faster detector
Faster SiPM
Faster scintillator + fibres
Faster electronics
Timing accuracy (ps)

## Slide 15: Challenges
Increase count-rate capability: 10 times more muons
Faster detector will help a bit

## Slide 16: Challenges
Solution: More detectors
Assembly of detectors: specialized work
Electronics?
96 detectors
1216 detectors

## Slide 17: Conclusion
Know how to build MuSR detectors
Future: 1) Faster detector components
      2) Large increase in number of detectors

## Slide 18: The end
Thank you very much for your attention